1.	PREAMBLE

When working in a recycled water environment, there is still a potential for exposure to a wide range of illnesses and infections, even though it has been treated to lower health risks (compared to raw sewage). Contact with recycled water by ingestion, inhalation of mist, or on cuts or abrasions should be avoided, and the precautionary measures listed below should be carefully reviewed and followed.

- SCOPE

Where activities are undertaken in areas or on infrastructure that is exposed or potentially exposed to recycled water, particularly in reuse applications.  These Guidelines generally relate to the use of recycled water provided as Class C (in accordance with the EPA Guidelines  464.2 “The reuse of wastewater”, 2003).  Work practices must be in accordance with these guidelines, any relevant Site/Environment Management Plan, and associated safe working instructions.

3.	PURPOSE

To advise staff, contractors, re-users, leasees, visitors and any other people potentially in contact with recycled water to minimise their risk of illnesses and infections through exposure to recycled water.

4.	INFECTIONS

Infectious agents like bacteria and viruses can enter the body via the skin, mouth and nose.  For more information on the transmission of diseases associated with recycled water, consult a medical specialist.

5.	PERSONAL PROTECTIVE EQUIPMENT

Workers should be provided protective clothing when there will be more than casual contact with the recycled water.  Equipment to be provided appropriate to the task: -

- Gloves protect the skin and reduce the risk of penetrating injuries;

- Use a face shield if there is a risk of splashes to eyes, nose and mouth; and

- Waders, gumboots and overalls reduce skin exposure to treated effluent.

Cuts, abrasions, or skin irritations are to be protected from contact with recycled water, either by personal protective equipment, possibly including barrier creams where appropriate.

- PERSONAL HYGIENE PRACTICES

Appropriate personal hygiene practices should be obeyed to avoid contamination from recycled water: -

- Eating, drinking or smoking should not occur whilst working directly with treated effluent;

- Wash your hands prior to eating, drinking and smoking and before and after going to the toilet;

- Food should not be taken into areas still wet with recycled water;

- Keep your workplace, clothing, tools and equipment clean and free from contamination;

- Shower at the end of the day.

# MINIMISING CONTAMINATION BY RECYCLED WATER

To minimise the risk of contamination of recycled water, preventative measures are to be taken: -

- Regular immunisations should be provided in accordance with relevant workplace policies and/or advice from a doctor.

- Safe drinking water should be supplied for workers.  Where bottled water is provided, the water should be in contamination-proof containers and protected from reclaimed water and dust.

- Handwashing facilities should be provided consisting of potable water supply, handwashing soap, and single use sanitary paper towels.  The importance of handwashing should be stressed when working with reclaimed water, especially before eating, drinking or smoking.

- Workers should not be subjected to reclaimed water sprays, mists or aerosols.

- Workers should not apply reclaimed water by hand held nozzles or other hand held devices that can produce sprays, mists or aerosols unless wearing appropriate personal protective equipment.

- Workers should be notified when recycled water is in use.  Notification should include the posting of conspicuous warning signs with proper wording of sufficient size to be clearly read.

- An adequate first aid kit should be available on location.  Cuts or abrasions should be promptly washed, disinfected and bandaged.

8.	IN THE EVENT OF RECYCLED WATER CONTAMINATION

In the event of contamination with recycled water, the following measures should be adopted:

- Remove, separate and wash or dispose of contaminated clothing;

- Shower or wash down with copious amounts of water;

- Use eye wash if eyes are contaminated;

- If recycled water is ingested, then advice from a doctor should be sought immediately regarding a preventative dose of immunoglobulin against Hepatitis A, if you are not already immunised;

- Report the incident to your supervisor and complete an Incident /Accident Report form;

- If you develop any symptoms of nausea, vomiting, diarrhoea or fever, then immediately consult your doctor and inform him/her of your exposure to recycled water; &

- Carry out an accident investigation to identify and address contributory factors in order to prevent a recurrence.