| Parent Policy: | OH&S and Injury Management Policy |
| --- | --- |

PURPOSE

To ensure that asbestos removal is conducted in accordance with legislation, the GWMWater Class B non-friable asbestos removal licence, EPA requirements for transport and disposal of waste asbestos material and that the risk to employees and other person’s health is minimised

SCOPE

This procedure is applicable to any works requiring the removal, cutting or connecting to asbestos cement (AC) pipework.

METHOD

| STEPS IN THE PROCEDURE | REFERENCES | RESPONSIBILITY | RECORDS |
| --- | --- | --- | --- |
| 1 | Assess task at hand (repair, connection, cut in etc.) and identify risks prior to any work to uncover pipework. The remainder of this procedure assumes removal of a length(s) of AC pipe is required) | Hazard Management Procedure | Senior person on site | Complaint report or works order |
| 2 | Ensure the following records / documentation is available at the worksite: Employee Training record (wallet sized card) Copy of the GWMWater Class B Asbestos Licence Asbestos removal control plan Determine if notifications are required to Worksafe Victoria and/or persons occupying immediate and adjacent premises | Class B Asbestos Licence H06/00378 | Senior person on site | Completed form CMS/124 Asbestos control plan and record of removal Adjacent Premises notified by form CMS/125 or diary note if verbally advised Victorian Worksafe notified by form CMS/126 Asbestos removal pack in operational vehicles |
| 3 | If works are required (i.e. cutting) that may release asbestos fibres, create AC dust or pipe fragments, then appropriate PPE must be worn. NO POWERED OR DISC POWERED ABRASIVE SAWS ARE PERMITTED TO BE USED | PPE issue list GWMWater Safe Work Instruction – Asbestos Removal | Senior person on site | Completed form CMS/124 Asbestos control plan and record of removal |
| 4 | At completion of job all asbestos waste, disposable clothing and equipment and other contaminated material is wrapped in bags provide, and taken by GWMWater vehicle to skip provided at operational depots BULK MATERIAL FROM SKIPS IS REMOVED PERIODICALLY BY TRAINED/LICENCED CONTRACTOR IN EPA LICENCED TRUCK | GWMWater Safe work Instruction – Repair and Removal of Asbestos Cement Pipes | Senior person on site | Completed form CMS/124 Asbestos control plan and record of removal |
| 5 | Completed CMS/124 Asbestos Control Plan and Record of Removals returned for filing and retention for a period of 12 months. |  | Admin/Technical Officer (Operations) | Records on file |

DOCUMENTATION

References

- OHS Act 2004 s21(2)a

- OHS Regulations 2017 (Asbestos)

- Asbestos Removal Licence – H06/00378

- GWMWater Safe Work Instruction Asbestos Removal

Records

- Asbestos Control Plan and Record of Removal

- Notification of Persons occupying Adjacent Premises

- Notification to Victorian Worksafe

DEFINITIONS

The reader is directed to the corporation’s standard definitions.