- Purpose

The purpose of this safe work instruction is to provide guidance and advice to management, supervisors, employees and contractors of GWMWater in relation to safety issues and the procedures that are to be followed when entering Control Valve pits on the Wimmera Mallee Pipeline.

- Scope

The scope of this safe Work Instruction applies to Wimmera Mallee Pipeline Project Control Valve pits that are under the direct control of GWMWater.

3	RESPONSIBILITIES

Management, supervisors, employees and contractors of GWMWater are responsible for following this safe work instruction.

## PROCEDURE

    - Pre Start Team Meeting prior to commencing task

    - Review Control Valve Pit JRA to establish Safe Work Methods for entry

    - Complete SWMS prior to entry

4.1	General

Personal protective equipment (PPE)  required  prior to commencing task depending on assessment of task to be conducted within the Control Valve pit

- Two person minimum (Standby arrangement)

  - First Aid Level II qualified

  - First Aid kit on site

- Communications

  - Mobile phone (in service) or equivalent on site

- Fitness for task

  - Persons to enter must be fit for task

4.2	On arrival at Control Valve Pit

- Open both hatches on top of Control Valve pit for ventilation

- Turn on lights to Control Valve pit or use torch if necessary

- Check Communications are in service

- Put on PPE (Minimum PPE required is Hardhat, safety glasses, gloves, hearing protection, safety boots and safety harness)

- Connect fall arrestor to safety harness and vehicle

- Remove hatch fall protection green grating and lift ladder extension arms up, for entry

4.3	Upon Entry

- Inspect Control Valve pit for hazards (ie: Snakes, spiders, water)

- Control hazards

- Isolate energy (if applicable)

- Check in with Standby person (Select most suitable hatch area for good visual and communications)

- On completion of works, check all equipment is removed from Control Valve pit

# DOCUMENTATION

5.1	Reference

- Operations Uniform and Personal Protective Equipment/Clothing Procedure

  - Records

- CMS/3393 Control Valve Pit JRA Form

- DEFINITIONS

The reader is directed to the corporation’s standard definitions.