| Parent Policy: | OH&S and Injury Management Policy |
| --- | --- |

PURPOSE

To ensure that asbestos removal is conducted in accordance with legislation, the GWMWater Class B non-friable asbestos removal licence, EPA requirements for transport and disposal of waste asbestos material and that the risk to employees and other persons health is minimised.

SCOPE

This procedure is applicable to any works requiring the removal, cutting or connecting to asbestos cement (AC) pipework.

METHOD

| STEPS IN THE PROCEDURE | REFERENCES | RESPONSIBILITY | RECORDS |
| --- | --- | --- | --- |
| 1 | Assess task at hand (repair, connection, cut in etc.) and identify risks prior to any work to uncover pipework. The remainder of this procedure assumes removal of a length(s) of AC pipe is required) | Hazard Management Procedure | Senior person on site | Complaint report or works order |
| 2 | Ensure the following records / documentation is available at the worksite: Employee Training record (wallet sized card) Copy of the GWMWater Class B Asbestos Licence Digital or paper Asbestos removal control plan Determine if notifications are required to Worksafe Victoria and/or persons occupying immediate and adjacent premises | Class B Asbestos Licence H06/00378 | Senior person on site | Completed digital or paper form CMS/124 Asbestos control plan and record of removal Adjacent Premises notified by form CMS/125 or diary note if verbally advised Victorian Worksafe notified by form CMS/126 Asbestos removal pack in operational vehicles |
| 3 | If works are required (i.e. cutting) that may release asbestos fibres, create AC dust or pipe fragments, then appropriate PPE must be worn. NO POWERED OR DISC POWERED ABRASIVE SAWS ARE PERMITTED TO BE USED | PPE issue list GWMWater Safe Work Instruction – Asbestos Removal | Senior person on site | Completed digital or paper form CMS/124 Asbestos control plan and record of removal |
| 4 | At completion of job all asbestos waste, disposable clothing and equipment and other contaminated material is double wrapped in bags provided, and taken by GWMWater vehicle to asbestos waste bin provided at designated operational worksites. The wrapped Asbestos waste is removed every 60 days from the Asbestos waste bins, by an approved Pegasus contractor, who is a licensed Asbestos Class A removalist contractor, EPA transport waste trained, holder of a current EPA prescribed industrial waste transport permit, using EPA waste transport certificates and is transported to an approved Asbestos trade waste transfer station. | GWMWater Safe work Instruction – Repair and Removal of Asbestos Cement Pipes | Senior person on site | Completed digital or paper form CMS/124 Asbestos control plan and record of removal EPA waste transport certificate completed by Contractor on pick up and delivery to approved asbestos waste transfer station |
| 5 | Completed Digital Asbestos removal record in Tech 1 work order system or paper CMS/124 Asbestos Control Plan and Record of Removals and retain records. | GWMWater Safe Work Instruction – Asbestos Removal | Senior person on site | Records on the Tech 1 Workorder system and reports can be retrieved as requested in excel 1 format |
| 6 | Completed Asbestos EPA waste transport certificates are provided by contractor to GWMWater networks systems and planning staff and Manager | EPA Regulations | GWMWater Manager of Network Systems and Planning | Records on the Tech 1 Workorder system |

DOCUMENTATION

References

- OHS Act 2004 s21(2)a

- OHS Regulations 2017 (Asbestos)

- Environmental Protection Regulations

- Asbestos Removal Licence – H06/00378

- GWMWater Safe Work Instruction Asbestos Removal

Records

- Asbestos Control Plan and Record of Removal

- Digital Asbestos removal record on Workorder Tech1 system

- Notification of Persons occupying Adjacent Premises

- Notification to Victorian Worksafe

DEFINITIONS

The reader is directed to the corporation’s standard definitions.